Open Robotics

---
What Is Open Robotics?
- Open hardware
  - Arduino
  - Rasbperry Pi
- open software
  - Linux and
  - Robotics Operating System (ROS)
- Scalable
- Modular

---
Closed Source Challenge
- The robot is based upon an Invacare Ranger II MWD (circa 1995).
- Information on Cast Off Durable Medical Equipment (DME) is zealously guarded.
- The only option for the Hacker/Maker is to reverse engineer the FET driver network, and feed these logic lines to a dedicated microprocessor.

---
Communications Options
- Wifi – Either Direct or Via an onboard proxy. This system uses the former
- XBee – Low power Digital Transceiver with custom or USB interfaces
- Blue Tooth – Available and tested.

---
Sensors & Peripherals
- Parallax Ping sensor – Good Range
- IR Distance Sensors – Good Price
- Motor Tachometer Sensor – Closed Source
- Audio Via Proxy
- Video Via Proxy
- Motor Driven Scoop / Blade
- AC control peripheral

---
Cost
- Batteries
  - $180
- Sensors
  - $30
- Arduino mega
  - $60
- Software and DME
  - Free!

---
Major Issue
- Motor Control boards are closed source
- This is a serious barrier to the re-use of DME for Hackers/Makers
Major Design Goodness
Integration of UPS and Motor Control boards into a single unit is good synergy, and supplies 117 VAC for other systems/peripherals

---
Solutions
- Reverse engineering
  - Takes a long time to reverse engineer a board
  - Free with device
- Development of a universal Motor control board
  - Initial development cost
  - Cost of the board
[Speaker Notes: We are currently developing a universal Development board based on our work with the Snobot Board will cost >$80 retail l]

---
Scale the Software
The same software is used to run each of these robots
< --- RC Car
<--- Snowbot
Why not a hummer? ----->